PLASMOD documentation

Dr. E. Fable, Apr 2018
IPP Garching, DE

Purpose of the code

PLASMOD is a transport model for tokamak plasmas, where the steady-state condition (in the sense of no time-dependent terms in the equations) is simulated given in input gross engineering parameters and some requirements/constraints.

The code is written in Fortran 90 / 77 and can be run as a subroutine inside a generic Tokamak plant system code.

The code is very fast and gives out realistic plasma profiles which satisfy the constraints and are consistent with the given engineering parameters.

Inputs to the code:

!INPUTS with typical default values
        num%dtminmin=1.0d-9 !not used
        num%dtminmax=0.001 !not used
        num%dtmaxmax=100.0 !not used
        num%tolopt=0.0001 !not used
        num%etol=100.0d0 !not used
        num%etol0=100.d0 !not used
        num%etolm=100.0d0 !not used
        num%tolmax=0.1d0 !not used
        num%biggest=huge(kind(1.0d0)) !not used
      num%tol=0.00001d0 !tolerance to be reached, in % variation at each time step
        num%dtmin=0.001d0 !min time step
        num%dtmax=0.5d0 !max time step
        num%dt=0.01d0 !time step
        num%dtinc=2.d0 !decrease of dt
        num%Ainc=1.1d0 !increase of dt
        num%test=100000. !max iteration number
        num%tolmin=10.1d0 ! multiplier of etolm that should not be overcome
        num%eopt=0.1d0 !exponent of jipperdo
        num%dtmaxmin=0.1d0 !exponent of jipperdo2
        num%capA=0.1d0 !first radial grid point
        num%maxA=0.d0 !diagz 0 or 1
        num%dgy=1.e-5 !Newton differential
        num%i_modeltype=1 !1 - simple gyrobohm scaling
        num%i_equiltype=1 !1 - EMEQ, solve equilibrium with given q95, with sawteeth. 2- EMEQ, solve with given Ip, with sawteeth.
        num%nx=41 !number of interpolated grid points
        num%nxt=5 !number of reduced grid points
        num%nchannels=3 !leave this at 3
        num%ipedestal=2 !1 - fixed temperature pedestal ped%teped. 2 - Saarelma scaling
 num%i_impmodel=1 !impurity model: 0 - fixed concentration, 1 - concentration fixed at pedestal top, then fixed density.

    geom%A = 3.1d0 !aspect ratio R/a
    geom%R = 9.072d0 ! major radius in m
    geom%bt = 5.667 !magnetic field in T
    geom%k = 1.7513d0 !edge elongation
    geom%d = 0.383d0 !edge triangularity
    geom%k95 = 1.65d0 !edge elongation at 95% of flux
    geom%d95 = 0.333d0 !edge triangularity at 95% of flux
    geom%Ip = 19.6 ! plasma current in MA : USED if i_equiltype=2, q95 is used if i_equiltype=1
  geom%q95 = 3.5 !safety factor at 95% of flux, used if i_equiltype=1.
  geom%counter=0. !dont touch this

!this is just for first initialization
    geom%Aold = geom%A !aspect ratio
    geom%Rold = geom%R ! major radius in m
    geom%kold = geom%k !edge elongation
    geom%dold = geom%d !edge triangularity
    geom%Ipold = geom%ip !plasma current in MA : USED if equiltype=2, q95 is used if equiltype=1
    geom%btold = geom%bt !magnetic field

!composition
    comp%globtau(1) = 5. !tauparticle/tauE for D
    comp%globtau(2) = 5. !tauparticle/tauE for T
    comp%globtau(3) = 5. !tauparticle/tauE for He
    comp%globtau(4) = 5. !tauparticle/tauE for Xe
    comp%globtau(5) = 1. !tauparticle/tauE for Ar

    comp%psepplh_inf = 1.1 !Psep/PLH if below this, use q_heat to control this
    comp%psepplh_sup = 1.2 !Psep/PLH if above this, use Xe to control this via radiation, if not to be used, set a very very large value
    comp%psepb_q95AR = 1000.d0 !Psep B/qaR max value, use the minimum between, if not to be used, set a very very large value this and pseplh_sup
    comp%psep_r = 1000.d0 !Psep/R max value , if not to be used, set a very very large value
    comp%qdivt = 0. !divertor heat flux in MW/m^2, if 0, dont use SOL model, if positive (in MW/m^2), uses car to control this

    comp%car = 0. !argon concentration, used self-consistently if qdivt=0.
    comp%c_car = 10. !compression factor between div and core: e.g. 10 means there is 10 more Argon concentration in the divertor than in the core
    comp%cxe = 0. !xenon concentration, changed selfconsistently if psepplh_sup is non zero
    comp%che = 0.08 !helium concentration, calculated self-consistently if globtau(3)>0

    comp%fuelmix = 0.5d0 !fuel mix -> D = fuelmix*(ne-nZ), T = (1-fuelmix)*(ne-nZ)

    comp%pradpos = 0.d0 ! position after which radiation is counted 0. for tau and other global quantities, i.e. position after which radiation is "edge"
comp%pradfrac = 0.d0 ! Fraction of core radiation which is actually used, the rest goes into edge
inp0%f_gw=0.9 !pedestal top greenwald fraction
inp0%f_gws=0.5 !separatrix greenwald fraction

    ped%teped=5.5 !pedestal top temperature
    ped%tesep=0.3 !separatrix temperature
    ped%rho_t=0.96 !pedestal top position T
    ped%rho_n=0.96 !pedestal top position n
ped%pedscal = 1. ! multiplied pedestal scaling

inp0%Hfac_inp=1. !input H factor to be reached. If 0., this is not used and H is instead an output. This is radiation corrected H factor using pradpos

inp0%nbcdeff=5. !CD = this * PCD units: m*MA/MW (MA/m^2 * m^3/MW)
inp0%eccdeff=0.3 !CD = this * PCD * TE/NE !not used for now
inp0%pheatmax=200. !max allowed power for heating+CD+fusion control+q_control

inp0%V_loop=-1.e6 !target loop voltage. If lower than -1.e5, dont use this
inp0%f_ni=0. !required fraction of non inductive current, if 0, dont use this
inp0%pfus=0. !if 0., not used (otherwise it would be controlled with Pauxheat), if positive, add power q_fus to control fusion power
inp0%q_control=50. !power required for additional control (NTM, sawteeth, etc.)

inp0%pech=0.d0 !ech power !not used for now
inp0%pnbi=0.d0 !nbi power !this is heat if not specified
inp0%qheat=0.d0 !nbi power
inp0%qcd=0.d0 !nbi power
inp0%qfus=0.d0 !nbi power

!depositions and widths
inp0%x_heat(1)=0. !nbi
inp0%x_heat(2)=0. !ech
inp0%x_cd(1)=0. !nbi
inp0%x_cd(2)=0. !ech
inp0%x_fus(1)=0. !nbi
inp0%x_fus(2)=0. !ech
inp0%x_control(1)=0. !nbi
inp0%x_control(2)=0. !ech
inp0%dx_heat(1)=0.2 !nbi
inp0%dx_heat(2)=0.03 !ech
inp0%dx_cd(1)=0.2 !nbi
inp0%dx_cd(2)=0.03 !ech
inp0%dx_fus(1)=0.2 !nbi
inp0%dx_fus(2)=0.03 !ech
inp0%dx_control(1)=0.2 !nbi
inp0%dx_control(2)=0.03 !ech
inp0%nbi_energy=1000. !in keV !beam energy

inp0%spellet=0.d0 !pellet mass in particles of D in 10^19
inp0%fpellet=0.5d0 !pellet frequency in Hz !pellet source is computed as inp0%spellet*inp0%fpellet in p/s

!control derivatives (for internal calculations), suggested values
inp0%qnbi_psepfac=50. !dqnbi/d(1-Psep/PLH)
inp0%cxe_psepfac=1.e-5 !dcxe/d(1-Psep/PLH)
inp0%car_qdivt=1.e-6 !dcar/d(qdivt)

inp0%PLH =0. ! LH transition power, if 0 is computed inside PLASMOD
inp0%maxpauxor = 20. ! maximum allowed auxiliary power / R.

Outputs from the code:

! Outputs:

* scalars
geom%ip --> this is an output if q95 was an input
mhd%ip --> plasma current in MA

geom%q95 --> this is an output if ip was an input
mhd%q --> q95

comp%che --> Helium concentration (computed if globtau(3) is finite)
comp%cxe --> Xenon concentration (computed if comp%psepplh_sup finite)
comp%car --> Argon concentration (computed if comp%qdivt finite)

ped%teped --> computed if num%ipedestal=2
ped%nped --> computed according to inp0%fgw
ped%nsep --> computed according to inp0%fgws

mhd%equilcheck = 0. if equilibrium crashed, 1 if ok
mhd%betan : total beta_N (thermal + alphas)

loss%pfus : fusion power in MW (5* alpha power)
loss%taueff : confinement time taue in s
loss%H : H factor
tau_scal = loss%taueff/loss%H
loss%Wth : plasma thermal energy in MJ
loss%prad: total radiated power (core + edge) in MW
loss%pradedge: edge radiated power in MW
loss%pradcore: core radiated power in MW
loss%psync : total synchrotron power (MW)
loss%pbrehms : brehmstralung power MW
loss%pline: line radiation MW
loss%psepi: ion separatrix power MW
loss%piepv: volume averaged equipartition power MW/m^3
loss%peaux: effective auxiliary electron heating in MW
loss%piaux: effective auxiliary ion heating in MW

loss%pdiv : divertor power in MW/m^2

loss%Psep: separatrix power	MW
loss%PLH: LH transition power MW

loss%dfuelreq : requested fueling in p/s for D
loss%tfuelreq : requested fueling in p/s for T

loss%hepumpreq = He production globally in p/s (to be pumped)

mhd%vp : plasma volume in m^3
mhd%q_sep : separatrix q
mhd%vloop : loop voltage in V
mhd%fbs : bootstrap current fraction
mhd%f_ni : total non inductive current fraction (CD + bs)

i_flag = 1 if OK, -1 if not converged after itermax, -2 equilibrium crashed, 0 transport crashed

* profiles
radp%x : normalized coordinate r/a
radp%ne : electron density profile in 10^19 m^-3
radp%te : electorn temperature profile in keV
radp%ti : ion temperature profile in keV

radp%qprof : safety factor profile
radp%jpar : parallel current profile in MA/m^2
radp%jbs : bootstrap current profile
radp%jcd : current drive profile
radp%ipol : poloidal current R*BT profile in T*m
radp%psi : poloidal flux profile in Wb
radp%volum : plasma volum profile in m^3

Suggested usage for a system code:

- always set Psep_PLH inf to 1 if you want to stay in H-mode. If the plasma goes below that,	PLASMOD sets Xenon to 0 and instead pumps up NBI until PSEP = PLH

- Set either Psep/PLH_sup, Psep/R, or PSEPqBAR to some value. If the plasma is above that,	then PLASMOD puts Xe until Psep = one of the three conditions. If the plasma is below those	values, than Xe = 0 and Psep is whatever it is.

- qdivt = 0 to start, better to prescribe Argon concentration from some other SOL model	(although PLASMOD has its own).

- Hfac_inp is used if itransport model = 1, all other models will produce H as an output

- q_control is the power that PLASMOD will not modify. Can be given as input.

- pedestal model 2 is pedestal scaling from Samuli Saarelma. Pedestal model 1 is fixed Te	pedestal top assigned as input.

- equiltype 1 uses q95 to compute current, better than the reverse.

- impmodel 0 or 1 doesnt matter

- globtau(3) ~ 1-10. Important for He.

- f_ni or v_loop should be dictated by discharge duration (comes from SYS code). Better to	assign f_ni between 0 and 1.

More detailed documentation of the code:

Subroutine call

The subroutine call is:

call PLASMOD_EF(num,geom,comp,ped,inp0,radp,mhd,loss,i_flag)

Note this:
  type (geometry), intent(inout) :: geom
  type (composition), intent(inout) :: comp
  type (pedestal), intent(inout) :: ped
  type (inputs), intent(inout) :: inp0
  type (radial_profiles), intent(inout) :: radp
  type (MHD_EQ), intent(inout) :: mhd
  type (power_losses), intent(inout) :: loss
all inputs are also outputs because the code can change some of the inputs consistently with the requirements given in input, however this is clearly stated in the description of the inputs when it is necessary.

Structure of the code

The code is structured in this way:

 Initialization: definition of initial guess + first equilibrium computation

Main cycle

Output production

Main cycle:
Iteration j
Compute sources: Pe, Pi, Sn
Compute transport coefficients
Solve transport equations for Te, Ti, ne
Adapt pedestal profiles if needed
Compute new equilibrium
Is tolerance reached ? If yes, exit. If no, go back to iteration j+1